## Slide 1: Computer Networks II TCP Congestion Control TCP Tahoe and TCP Reno
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Network Congestion
Routers have input/output queue
  These queues get filled up  leads to congestion
Switch
fabric
Host A
Host B

## Slide 3: Effects of Congestion
Retransmitting undelivered packets: Packets can be lost, dropped at router due to full buffers
Retransmitting timeout packets: Sender timers can time out prematurely, sending two copies, both of which are delivered
  Decrease maximum achievable goodput
Host A
Host B
All link capacity = R
R/2

## Slide 4: Effects of Congestion
We want to operate just before the onset of congestion
  Avoid congestion
  Most capacity is used
  Needs to be fair across competitive flows
Host A
Host B
All link capacity = R
R/2

## Slide 5: Challenges of Congestion Control
How the senders will know whether there is a congestion or not?
No explicit feedback from network
  Congestion inferred from observed loss, delay
Host A
Host B

## Slide 6: Challenges of Congestion Control
The senders need to adapt/tune the sending rates to match the available bandwidth of the bottleneck link
  Sending rate= function (available bandwidth of the bottleneck link)
Which link has the lowest available bandwidth?
  Sender does not have the global picture
Available bandwidth varies with time
  Number of flows and their offered load is dynamic
  Bottleneck link can also vary
Time
Bandwidth
Capacity

## Slide 7: Challenges of Congestion Control
The senders need to adapt/tune the sending rates to match the available bandwidth of the bottleneck link
  Sending rate= function (available bandwidth of the bottleneck link)
Which link has the lowest available bandwidth?
  Sender does not have the global picture
Available bandwidth varies with time
  Number of flows and their offered load is dynamic
  Bottleneck link can also vary

## Slide 8: Challenges of Congestion Control
The senders need to adapt/tune the sending rates to match the available bandwidth of the bottleneck link
  Sending rate= function (available bandwidth of the bottleneck link)
Which link has the lowest available bandwidth?
  Sender does not have the global picture
Available bandwidth varies with time
  Number of flows and their offered load is dynamic
  Bottleneck link can also vary

## Slide 9: TCP Congestion Control
TCP sender limits transmission:
LastByteSent - LastByteAcked  cwnd
last byte
ACKed
last byte sent
cwnd
sender sequence number space
available but not used
TCP sending behavior : send cwnd bytes, wait RTT for ACKS, then send more bytes
TCP rate
~
~
cwnd
RTT
bytes/sec
sent, but not-yet ACKed
(“in-flight”)
Senders need to adapt/tune the sending rate
  How many bytes are inside the network  called congestion window or cwnd
cwnd is dynamically adjusted in response to observed network congestion  Implementing TCP congestion control

## Slide 10: TCP Congestion Control: AIMD
Approach: Senders can increase sending rate until packet loss (congestion) occurs, then decrease sending rate on loss event
AIMD sawtooth
behavior: probing
for bandwidth
TCP sender Sending rate
Time
  Additively increase rate until network is not congested
Additive Increase
  Multiplicatively decrease rate when congestion occurs
Multiplicative Decrease

## Slide 11: TCP Tahoe

## Slide 12: TCP slow start
Host A
one segment
Host B
RTT
two segments
four segments
Assumption: 1 MSS = 1 Byte
1 2 3 4 5 6 7 8
CW = 1
1 2 3 4 5 6 7 8
CW = CW + 1 = 2
1 2 3 4 5 6 7 8
CW = CW + 1 = 3
B1
A2
B2
B3
A3
B4
B5
B6
B7
A4
1 2 3 4 5 6 7 8
CW = CW + 1 = 4
Host A
Host B
RTT
Slow start (cwnd = 1 MSS)
CW is doubling in every RTT  exponential increase of CW

## Slide 13: TCP Slow Start
When connection begins, increase rate exponentially until first loss event:
  Initially cwnd = 1 MSS
  Double cwnd every RTT
  Done by incrementing cwnd for every ACK received
Host A
one segment
Host B
RTT
time
two segments
four segments
Summary: Initial rate is slow, but ramps up exponentially fast

## Slide 14: TCP Congestion Avoidance
After ssthresh, reduce the rate of CW increase
1 2 3 4 5 6 7 8
CW = 1
1 2 3 4 5 6 7 8
CW = CW + 1 = 2
1 2 3 4 5 6 7 8
CW = CW + 1 = 3
B1
A2
B2
B3
A3
B4
B5
A4
Host A
Host B
Upon every ACK
CW = CW + MSS
= CW +
B4
B5
B6
B7
A4
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 1/4
Host A
Host B
A5
A6
A7
A8
B8
B9
B10
B11
B12
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 2/4
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 3/4
1 2 3 4 5 6 7 8
CW = CW + 1 = 4
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 4/4 = 5

## Slide 15: TCP Congestion Avoidance
After ssthresh, reduce the rate of CW increase
Upon every ACK
CW = CW + MSS
= CW +
B4
B5
B6
B7
A4
Host A
Host B
A6
A7
A8
B8
B9
B10
B11
B12
Host A
one segment
Host B
RTT
two segments
four segments
RTT
RTT
CW = 1
CW = 2
CW = 4
CW = 5
After 1 RTT, the CW is approx. increasing by 1 MSS  Congestion avoidance
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 1/4
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 2/4
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 3/4
1 2 3 4 5 6 7 8 9 10 11 12 13
CW = 4 + 4/4 = 5
1 2 3 4 5 6 7 8
CW = CW + 1 = 4

## Slide 16: TCP Congestion Avoidance
After ssthresh, reduce the rate of CW increase
Upon every ACK
CW = CW + MSS
= CW +
Host A
one segment
Host B
RTT
two segments
four segments
RTT
RTT
CW = 1
CW = 2
CW = 4
CW = 5
After 1 RTT, the CW is approx. increasing by 1 MSS  Congestion avoidance
If MSS = 1460 Bytes, CW = 14600 Bytes
 CW = CW + MSS
 CW will be increased by 1 MSS after all 10 segments will be received  after 1 RTT

## Slide 17: TCP Congestion Avoidance
After ssthresh, reduce the rate of CW increase
Host A
one segment
Host B
RTT
two segments
four segments
RTT
RTT
CW = 1
CW = 2
CW = 4
CW = 5
After 1 RTT, the CW is approx. increasing by 1 MSS  Congestion avoidance

## Slide 18: Packet/ACK Drop
TX infers a packet loss  goes to slow start 
Host B
Host A
timeout
Host B
Host A
X
timeout
X
Host B
Host A
X
B1
B1
A2
B1
A2
B2
A3
timeout
CW = 2
CW = 4

## Slide 19: TCP Fast Retransmit
Host B
Host A
timeout
A5
A5
A5
A5
B6
B7
B8
B5
X
If sender receives 3 duplicate ACKs:
  Likely that unACKed segment lost, so don’t wait for timeout
  Resend unACKed segment with smallest seq #
B5
Notes: Let’s wrap up our study of TCP reliability by discussing an optimization to the original TCP known as TCP fast retransmit,
Take a look at this example on the right where 5 segments are transmitted and the second segment is lost. In this case the TCP receiver sends an ACK 100 acknowledging the first received segment.
When the third segment arrives at the receiver, the TCP receiver sends another ACK 100 since the second segment has not arrived. And similarly for the 4th and 5th segments to arrive.
Now what does the sender see? The sender receives the first ACK 100 it has been hoping for, but then three additional duplicate ACK100s arrive. The sender knows that somethings’ wrong – it knows the first segment arrived at the receiver but three later arriving segments at the receiver – the ones that generated the three duplicate ACKs – we received correctly but were not in order. That is, that there was a missing segment at the receiver when each of the three duplicate ACK were generated.
With fast retransmit, the arrival of three duplicate ACK causes the sender to retransmit its oldest unACKed segment, without waiting for a timeout event. This allows TCP to recover more quickly from what is very likely a loss event
specifically that the second segment has been lost, since three higher -numbered segments were received

## Slide 20: TCP Tahoe: Slow start followed by additive increase
X

## Slide 21: TCP Tahoe
Timeout or 3 Duplicate ACK
ssthresh = cwnd/2
cwnd = 1 MSS
retransmit missing segment
L
cwnd > ssthresh
Congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
transmit new segment(s), as allowed
new ACK
.
Slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
retransmit missing segment
cwnd = cwnd+MSS
transmit new segment(s), as allowed
new ACK
L
cwnd = 1 MSS
ssthresh = 64 KB

## Slide 22: TCP Reno

## Slide 23: Fast Recovery
3 DupACks
Trigger Fast Retransmit
1. Ssthresh = CW/2
2. Transmit missing segment that is definitely causing DupAcks
3. CW = ssthresh + 3
4. Transmit new segments of CW allows
5. More DupAcks:
CW = CW + 1
Transmit new segments if CW allows
6. Normal ACK:
CW = ssthresh
Start congestion avoidance
Host B
Host A
timeout
B11
B12
A5
A5
A5
A5
Host B
Host A
A5
A5
A5
A10
B5
B9
B6
B7
B8
B5

## Slide 24: TCP Reno vs TCP Tahoe
Src: https://commons.wikimedia.org/wiki/File:CongWin_in_TCP_Tahoe_e_Reno.png

## Slide 25: TCP Reno vs TCP Tahoe
Src: https://www.sfu.ca/~ljilja/papers/WM-195.PacketControl_edited.pdf

## Slide 26: TCP Reno: TCP Tahoe + Fast recovery
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
Congestion
avoidance
cwnd = cwnd + MSS  (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
Fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
Slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0

## Slide 27: TCP Throughput
Avg. TCP throughput as function of window size, RTT?
  Ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  Avg. window size (# in-flight bytes) is ¾ W
  Avg. throughput is 3/4W per RTT
W
W/2
Avg TCP throughput =
3
4
W
RTT
bytes/sec

## Slide 28: Summary
Network congestion control:
  Challenges of congestion
  TCP congestion control
    TCP Tahoe and TCP Reno