## Slide 1: Computer Networks TCP Connection Management
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: TCP Segment Structure
Source port #
Dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
Sequence number
segment seq #: counting bytes of data into bytestream (not segments!)
Application data
(variable length)
data sent by application into TCP socket
A
Acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification

## Slide 3: TCP Connection Management
Before exchanging data, sender/receiver “handshake”:
Agree to establish connection (each knowing the other willing to establish connection)
Agree on connection parameters (e.g., starting seq #s)
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Notes: The other TCP topic we’ll want to consider here is that of “connection management”
The TCP sender and reciver have a number of pieces of shared state that they must establish before actually communication
FIRST theym ust both agree that they WANT to communicate with each other
Secondly there are connection parameters – the initial sequence number and the initial receiver-advertised bufferspace that they’ll want to agree on
This is done via a so-called handshake protocol – the client reaching our to the server, and the server answering back.
And before diving into the TCP handshake protocol, let’s first consider the problem of handshaking, of establishing shared state.

## Slide 4: Agreeing to Establish a Connection
Will 2-way handshake always work in network?
Variable delays
Retransmitted messages (e.g. req_conn(x)) due to message loss
Message reordering
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
Notes: Here’s an example of a two way handshake. Alice reaches out to Bob and say’s “let’s talk” and Bob says OK, and they start their conversation
For a network protocol, the equivalent protocol would be a client sending a “request connection” message saying ”let’s talk, the initial sequence number is x”
And the server would respond with a message ”I accept your connect x”
And the question we want to ask ourselves is <talk through>
Will this work? Let’s look at a few scenarios…

## Slide 5: 2-way Handshake Scenarios
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
ACK(x+1)
No problem!
ESTAB
retransmit
req_conn(x)
req_conn(x)
client terminates
server
forgets x
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
acc_conn(x)
Problem: half open connection! (no client)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
Problem: dup data
accepted!
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
retransmit
req_conn(x)
ESTAB
req_conn(x)

## Slide 6: TCP 3-way Handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
Client state
Server state
LISTEN
x and y are chosen randomly
Notes: TCP’s three way handshake, that operates as follows
Let’s say the client and server both create a TCP socket as we learned about in Chapter 2 and enter the LISTEN state
The client then connects to the server sending a SYN message with a sequence number x (SYN Message is an TCP Segment with SYN but set in the header – you might want to go back and review the TCP segment format!)
The server is waiting for a connection, and receives the SYN message enters the SYN received state (NOT the established state and sends a SYN ACK message back.
Finally the client sends an ACK message to the server, and when the server receiver this enters the ESTABLished state. This is when the application process would see the return from the wait on the socket accept() call

## Slide 7: TCP State Diagram
Src: https://en.wikipedia.org/wiki/File:Tcp_state_diagram.png
SYNbit=1, Seq=x
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
ACKbit=1, ACKnum=y+1
SYNSENT
ESTAB
SYN RCVD
Client state
Server state
LISTEN
Notes: All good things must come to an end, and that’s true for a TCP connection as well.
And of course there’s a protocol for one side to gracefully close of a TCP connection using a FIN message, to which the other side sends a FINACK message and waits around a bit to respond to any retransmitted FIN messages before timing out.

## Slide 8: TCP 3-way Handshake
ESTAB
retransmit
req_conn(x)
req_conn(x)
client terminates
server
forgets x
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
acc_conn(x)
retransmit
SYN
client terminates
server
forgets x
connection
x completes
choose x
SYN,Seq=x
ESTAB
ESTAB
SYNACK,
Seq=y,ACK=x+1
ACK, ACK=y+1
SYNACK,
Seq=z,ACK=x+1
RST,ACK=z+1
🤔
SYN,Seq=x
RST: Abort connection
Receiver is confused
  Unexpected sequence number
  Port number or IP address do not match with any ongoing sockets
How it will solve the “half-open connection” problem?
SYN
RCVD
SYN
RCVD

## Slide 9: TCP 3-way Handshake
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
retransmit
req_conn(x)
ESTAB
req_conn(x)
RST: Abort connection
Receiver is confused
  Unexpected sequence number
  Port number or IP address do not match with any ongoing sockets
client terminates
ESTAB
choose x
ESTAB
accept
data(x+1)
connection
x completes
server
forgets x
retransmit
data(x+1)
retransmit
req_conn(x)
SYN,Seq=x
SYNACK,
Seq=y,ACK=x+1
ACK,Seq=x+1,
ACK=y+1,DATA
SYN,Seq=x
SYNACK,
Seq=z,ACK=x+1
ACK,Seq=x+1,
ACK=y+1,DATA
RST,ACK=z+1
🤔
🤔
How it will solve the “duplicate data accept” problem?
SYN
RCVD
SYN
RCVD

## Slide 10: Initial Sequence Number
Initial sequence numbers are chosen randomly
Why not 0?
  Segments of different connections can get mixed up
  Security issues when sequence numbers are predictable
ESTAB
retransmit
SYN
client terminates
server
forgets x
connection
x completes
choose x
SYN,Seq=x
ESTAB
ESTAB
SYNACK,
Seq=y,ACK=x+1
ACK,
Seq=x+1.ACK=y+1
SYNACK,
Seq=z,ACK=x+1
RST,ACK=z+1
🤔
SYN,Seq=x
client terminates
ESTAB
choose x
ESTAB
accept
data(x+1)
connection
x completes
server
forgets x
retransmit
data(x+1)
retransmit
req_conn(x)
SYN,Seq=x
SYNACK,
Seq=y,ACK=x+1
ACK,Seq=x+1,
ACK=y+1,DATA
SYN,Seq=x
SYNACK,
Seq=z,ACK=x+1
ACK,Seq=x+1,
ACK=y+1.DATA
RST,ACK=z+1
🤔
🤔
SYN
RCVD
SYN
RCVD

## Slide 11: Closing a TCP Connection
Client, server each close their side of connection
  Send TCP segment with FIN bit = 1
Respond to received FIN with ACK
  On receiving FIN, ACK can be combined with own FIN
All resources on the client side (including port number) are released
Src: https://commons.wikimedia.org/wiki/File:Tcp_close.svg
Notes: All good things must come to an end, and that’s true for a TCP connection as well.
And of course there’s a protocol for one side to gracefully close of a TCP connection using a FIN message, to which the other side sends a FINACK message and waits around a bit to respond to any retransmitted FIN messages before timing out.

## Slide 12: Closing a TCP Connection
Symmetric connection termination
  Both side should release separately
  B may have some data to transmit
TIME_WAIT varies from 30 secs - 2 mins
  Typically equal to 2 x Max time an IP datagram might live in the Internet
  Final ACK may be lost
    B may retransmit the FIN
    A can resend final ACK in case it is lost
    The second FIN may get delayed
    Another pair of processes may open the connection (with same port numbers)
    The delayed FIN may initiate an unwanted termination
Src: https://commons.wikimedia.org/wiki/File:Tcp_close.svg
Case-1:
Case-2:
Notes: All good things must come to an end, and that’s true for a TCP connection as well.
And of course there’s a protocol for one side to gracefully close of a TCP connection using a FIN message, to which the other side sends a FINACK message and waits around a bit to respond to any retransmitted FIN messages before timing out.

## Slide 13: TCP State Diagram
Src: https://en.wikipedia.org/wiki/File:Tcp_state_diagram.png
Src: https://commons.wikimedia.org/wiki/File:Tcp_close.svg
Notes: All good things must come to an end, and that’s true for a TCP connection as well.
And of course there’s a protocol for one side to gracefully close of a TCP connection using a FIN message, to which the other side sends a FINACK message and waits around a bit to respond to any retransmitted FIN messages before timing out.

## Slide 14: Summary
TCP connection management:
  Connection setup  3-way handshake
  Connection termination  Symmetric release